Motorola 68000 Instruction Set.
-------------------------------

                                                               Condition Codes
                                                               ---------------
                                          Assembler   Data
Instruction Description                    Syntax     Size        X N Z V C
-----------------------                   ---------   ----        ---------

ABCD     Add BCD with extend                Dx,Dy      B--        * U * U *
                                         -(Ax),-(Ay)
ADD      ADD binary                        Dn,<ea>     BWL        * * * * *
                                           <ea>,Dn
ADDA     ADD binary to An                  <ea>,An     -WL        - - - - -
ADDI     ADD Immediate                     #x,<ea>     BWL        * * * * *
ADDQ     ADD 3-bit immediate             #<1-8>,<ea>   BWL        * * * * *
ADDX     ADD eXtended                       Dy,Dx      BWL        * * * * *
                                         -(Ay),-(Ax)
AND      Bit-wise AND                      <ea>,Dn     BWL        - * * 0 0
                                           Dn,<ea>
ANDI     Bit-wise AND with Immediate    #<data>,<ea>   BWL        - * * 0 0
ASL      Arithmetic Shift Left            #<1-8>,Dy    BWL        * * * * *
                                            Dx,Dy
                                            <ea>
ASR      Arithmetic Shift Right              ...       BWL        * * * * *
Bcc      Conditional Branch            Bcc.S <label>   BW-        - - - - -
                                       Bcc.W <label>
BCHG     Test a Bit and CHanGe             Dn,<ea>     B-L        - - * - -
                                        #<data>,<ea>
BCLR     Test a Bit and CLeaR                ...       B-L        - - * - -
BSET     Test a Bit and SET                  ...       B-L        - - * - -
BSR      Branch to SubRoutine          BSR.S <label>   BW-        - - - - -
                                       BSR.W <label>
BTST     Bit TeST                          Dn,<ea>     B-L        - - * - -
                                        #<data>,<ea>
CHK      CHecK Dn Against Bounds           <ea>,Dn     -W-        - * U U U
CLR      CLeaR                              <ea>       BWL        - 0 1 0 0
CMP      CoMPare                           <ea>,Dn     BWL        - * * * *
CMPA     CoMPare Address                   <ea>,An     -WL        - * * * *
CMPI     CoMPare Immediate              #<data>,<ea>   BWL        - * * * *
CMPM     CoMPare Memory                  (Ay)+,(Ax)+   BWL        - * * * *
DBcc     Looping Instruction          DBcc Dn,<label>  -W-        - - - - -
DIVS     DIVide Signed                     <ea>,Dn     -W-        - * * * 0
DIVU     DIVide Unsigned                   <ea>,Dn     -W-        - * * * 0
EOR      Exclusive OR                      Dn,<ea>     BWL        - * * 0 0
EORI     Exclusive OR Immediate         #<data>,<ea>   BWL        - * * 0 0
EXG      Exchange any two registers         Rx,Ry      --L        - - - - -
EXT      Sign EXTend                         Dn        -WL        - * * 0 0
ILLEGAL  ILLEGAL-Instruction Exception     ILLEGAL                - - - - -
JMP      JuMP to Affective Address          <ea>                  - - - - -
JSR      Jump to SubRoutine                 <ea>                  - - - - -
LEA      Load Effective Address            <ea>,An     --L        - - - - -
LINK     Allocate Stack Frame       An,#<displacement>            - - - - -
LSL      Logical Shift Left                 Dx,Dy      BWL        * * * 0 *
                                          #<1-8>,Dy
                                            <ea>
LSR      Logical Shift Right                 ...       BWL        * * * 0 *
MOVE     Between Effective Addresses      <ea>,<ea>    BWL        - * * 0 0
MOVE     To CCR                           <ea>,CCR     -W-        I I I I I
MOVE     To SR                             <ea>,SR     -W-        I I I I I
MOVE     From SR                           SR,<ea>     -W-        - - - - -
MOVE     USP to/from Address Register      USP,An      --L        - - - - -
                                           An,USP
MOVEA    MOVE Address                      <ea>,An     -WL        - - - - -
MOVEM    MOVE Multiple            <register list>,<ea> -WL        - - - - -
                                  <ea>,<register list>
---------- Page 2. CUT HERE. ----------
MOVEP    MOVE Peripheral                  Dn,x(An)     -WL        - - - - -
                                          x(An),Dn
MOVEQ    MOVE 8-bit immediate         #<-128.+127>,Dn  --L        - * * 0 0
MULS     MULtiply Signed                   <ea>,Dn     -W-        - * * 0 0
MULU     MULtiply Unsigned                 <ea>,Dn     -W-        - * * 0 0
NBCD     Negate BCD                         <ea>       B--        * U * U *
NEG      NEGate                             <ea>       BWL        * * * * *
NEGX     NEGate with eXtend                 <ea>       BWL        * * * * *
NOP      No OPeration                        NOP                  - - - - -
NOT      Form one's complement              <ea>       BWL        - * * 0 0
OR       Bit-wise OR                       <ea>,Dn     BWL        - * * 0 0
                                           Dn,<ea>
ORI      Bit-wise OR with Immediate     #<data>,<ea>   BWL        - * * 0 0
PEA      Push Effective Address             <ea>       --L        - - - - -
RESET    RESET all external devices         RESET                 - - - - -
ROL      ROtate Left                      #<1-8>,Dy    BWL        - * * 0 *
                                            Dx,Dy
                                            <ea>
ROR      ROtate Right                        ...       BWL        - * * 0 *
ROXL     ROtate Left with eXtend             ...       BWL        * * * 0 *
ROXR     ROtate Right with eXtend            ...       BWL        * * * 0 *
RTE      ReTurn from Exception               RTE                  I I I I I
RTR      ReTurn and Restore                  RTR                  I I I I I
RTS      ReTurn from Subroutine              RTS                  - - - - -
SBCD     Subtract BCD with eXtend           Dx,Dy      B--        * U * U *
                                         -(Ax),-(Ay)
Scc      Set to -1 if True, 0 if False      <ea>       B--        - - - - -
STOP     Enable & wait for interrupts      #<data>                I I I I I
SUB      SUBtract binary                   Dn,<ea>     BWL        * * * * *
                                           <ea>,Dn
SUBA     SUBtract binary from An           <ea>,An     -WL        - - - - -
SUBI     SUBtract Immediate                #x,<ea>     BWL        * * * * *
SUBQ     SUBtract 3-bit immediate       #<data>,<ea>   BWL        * * * * *
SUBX     SUBtract eXtended                  Dy,Dx      BWL        * * * * *
                                         -(Ay),-(Ax)
SWAP     SWAP words of Dn                    Dn        -W-        - * * 0 0
TAS      Test & Set MSB & Set N/Z-bits      <ea>       B--        - * * 0 0
TRAP     Execute TRAP Exception           #<vector>               - - - - -
TRAPV    TRAPV Exception if V-bit Set       TRAPV                 - - - - -
TST      TeST for negative or zero          <ea>       BWL        - * * 0 0
UNLK     Deallocate Stack Frame              An                   - - - - -

                           --------------------------

Symbol   Meaning
------   -------

   *     Set according to result of operation
   -     Not affected
   0     Cleared
   1     Set
   U     Outcome (state after operation) undefined
   I     Set by immediate data

<ea>     Effective Address Operand
<data>   Immediate data
<label>  Assembler label
<vector> TRAP instruction Exception vector (0-15)
<rg.lst> MOVEM instruction register specification list
<displ.> LINK instruction negative displacement
...      Same as previous instruction

                           --------------------------
---------- Page 3. CUT HERE. ----------
Addressing Modes                                   Syntax
----------------                                   ------

Data Register Direct                                 Dn
Address Register Direct                              An
Address Register Indirect                           (An)
Address Register Indirect with Post-Increment       (An)+
Address Register Indirect with Pre-Decrement        -(An)
Address Register Indirect with Displacement         w(An)
Address Register Indirect with Index               b(An,Rx)
Absolute Short                                        w
Absolute Long                                         l
Program Counter with Displacement                   w(PC)
Program Counter with Index                         b(PC,Rx)
Immediate                                            #x
Status Register                                      SR
Condition Code Register                              CCR

Legend
------
   Dn    Data Register        (n is 0-7)
   An    Address Register     (n is 0-7)
    b    08-bit constant
    w    16-bit constant
    l    32-bit constant
    x    8-, 16-, 32-bit constant
   Rx    Index Register Specification, one of:
            Dn.W  Low 16 bits of Data Register
            Dn.L  All 32 bits of Data Register
            An.W  Low 16 bits of Address Register
            An.L  All 32 bits of Address Register

                           --------------------------

         Condition Codes for Bcc, DBcc and Scc Instructions.
         ---------------------------------------------------

           Condition Codes set after CMP D0,D1 Instruction.

Relationship      Unsigned                         Signed
------------      --------                         ------

D1 <  D0          CS - Carry Bit Set               LT - Less Than
D1 <= D0          LS - Lower or Same               LE - Less than or Equal
D1  = D0          EQ - Equal (Z-bit Set)           EQ - Equal (Z-bit Set)
D1 != D0          NE - Not Equal (Z-bit Clear)     NE - Not Equal (Z-bit Clear)
D1 >  D0          HI - HIgher than                 GT - Greater Than
D1 >= D0          CC - Carry Bit Clear             GE - Greater than or Equal

                  PL - PLus (N-bit Clear)          MI - Minus (N-bit Set)
                  VC - V-bit Clear (No Overflow)   VS - V-bit Set (Overflow)
                  RA - BRanch Always

DBcc Only    -     F - Never Terminate (DBRA is an alternate to DBF)
                   T - Always Terminate

Scc Only     -    SF - Never Set
                  ST - Always Set

                           --------------------------

Parts from "Programming the 68000" by Steve Williams. (c) 1985 Sybex Inc.
Parts from BYTE Magazine article.

Compiled by Diego Barros.        e-mail : alien@zikzak.apana.org.au
Revision 2.1                     22 May, 1994
---------- Last Page. CUT HERE. ----------